## Slide 1: Multiple Robot navigation and Mapping for Combat environment
By: Scott Tipton and Nick Halabi
Advisor: Dr. Aleksander Malinowski
Bradley University
December 3, 2010

## Slide 2: Outline
Project Summary
Previous Work
Project Description
System Overview
Subsystems
  Work completed and important equations
Equipment and Parts List
Progress
Schedule of Tasks

## Slide 3: Project Summary
Military application – proof of concept
Combat/unknown environment
  Indoor or outdoor
Map area and detect potential threats
Guide autonomous supply caravans or troops safely through a combat zone

## Slide 4: System Platform
Pioneer 3D-X
  8 Sonar sensors (+90 to -90)
  2 wheels for navigation, 1 for stability
Navigation Computer (Laptop)
  C++ program with Visual Studio 2005
  Aria
  MobileSim

## Slide 5: Goals
Robot Navigating
  Sonar Sensors
  IR Sensors
Environment Mapping
  Metal Detector
Path Finding
Server Infrastructure
Localization

## Slide 6: Previous Work
IR sensors integration
Dr. Malinowski’s mapping program
  Updated by John Hessling

## Slide 7: Project Description
First robot scans and maps environment
Second robot uses path finding algorithm to designate safe route
Server/Central command
  Pass information (map files)
  User override via joystick

## Slide 8: System Overview

## Slide 9: Subsystems – Mode 1
Find closest wall and drive to it
Use wall following algorithm
Perform random movement when finished to scan interior
  Optional operator override
Map environment
  Detect threats with metal detectors
Relay map to server

## Slide 10: Mode 1 – Trigonometry

## Slide 11: Mode 1 – Equations
Wall distance
  (a*b*sin(20/rad_to_deg))/sqrt(a^2*+b^2-2*a*b*cos(20/rad_to_deg))
  (a*b*sin(20/rad_to_deg))/c
Move parallel to wall
  angle = asin(height/a)*rad_to_deg +10
  angle = 180 - angle;
Wall following
  error = (((xr90 + ideal_distance)/2)-xr90)

## Slide 12: Mode 1 – Mapping

## Slide 13: Subsystems – Server
Maintain constant connection with both robots
Receive and update map from mode 1
Relay map to mode 2
User override with joystick control

## Slide 14: Subsystems - Mode 2
Read map from server
Path Planning - determine safest route
Navigate to destination

## Slide 15: Mode 2 – Path Planning
Grassfire approach
Obstacles – 32,000
Non-reachable – 0

## Slide 16: Path Planning

## Slide 17: Path Planning

## Slide 18: Equipment and Parts List
Pioneer 3D-X
Metal detectors – Electronics123.com Product # Velleman K7102
IR sensors - Sharp GP2Y0A02YK0F
Force Feedback Joystick
Silicon Labs 80C51F120 + UART/USB adaptor

## Slide 19: Velleman Metal Detectors
Kit- Requires Soldering
Metal detecting distance adjustable: up to 3.15"
We will use 4 detectors on the mapping robot
This will be a proof of concept, to see if we can detect mines

## Slide 20: Progress
Mode 1 – 70% Complete
  Mapping and navigation
  Manual override with joystick
  Metal Detector
  Improve wall following
Mode 2 – 50%
  Path planning using the grassfire approach
  Possibly use the potential field approach or a combination of the two
Server – 0%

## Slide 21: Schedule of Tasks
12/17/2009 – 1/20/2010
Improve wall following algorithm
Develop potential field path planning
Start server setup
Setup testing environments
1/21/2010 – 2/11/2010
Continue server work
Begin integrating metal detector sensors and possible IR sensors
2/18/2010 – 3/11/2010
Work with Mike Firman
Implement force feedback joysticks
Localization if time permits.
3/13/2010 – 3/22/2010
Spring break
Begin final presentation
Conference paper

## Slide 22: Questions?