## Slide 1: Variable Frequency AC Source
Students:
Kevin Lemke
Matthew Pasternak
Advisor:
Steven D. Gutschlag

## Slide 2: Project Goals
Variable Frequency AC Source (VFACS)
Capable of delivering 208 Vrms and 5 A (35.5V rms for initial testing)
Frequency range from 0 to 60 Hz

## Slide 3: High Level System Block Diagram

## Slide 4: PWM Generation Controller
Produces PWM signals for the Gate Drive Circuitry
Use a LabVIEW based cDAQ controller from National Instruments
Able to control both single phase and three phase systems

## Slide 5: PWM Generation Controller

## Slide 6: PWM Generation Controller
Produce TTL level PWM signals
Produce waveforms representative of sine waves from 0-60 Hz
Produce waveforms following proper V/Hz ratio of 0.5892

## Slide 7: Gate Drive Circuitry
High speed signal isolator and driver
Use optical isolators and gate driver chips to isolate and amplify signal to the Inverter
Optical isolators and gate drivers chosen for speed and robustness

## Slide 8: Gate Drive Circuitry

## Slide 9: Gate Drive Circuitry
Along with inverter, capable of switching at 1% duty cycle of 15 kHz switching frequency without clipping
Optical Isolator
  6N137 Optocoupler
  Isolate cDAQ outputs from Inverter, Filter, and Load
Gate Driver
  IR-2110
  Amplify PWM from TTL to +15V 2A level adequate for driving the Inverter

## Slide 10: Gate Drive Circuitry Changes
Replaced IR2110/6n137 with HCPL3120
  Robustness
  Real-estate
  Simplicity
Verify that this chip would meet specifications
  Speed capability
  Drive capability
www.avagotech.com/docs/AV02-0161EN

## Slide 11: Inverter
PWM Signal Amplifier for AC machine application
Use IGBT pairs and DC rails to amplify PWM signal
IGBTs used for high voltage capabilities and availability
Single- and three-phase configurations

## Slide 12: Inverter

## Slide 13: Inverter

## Slide 14: Inverter
Single-phase Inverter
  Fairchild FMG2G75US60 IGBT Pair
  Each IGBT will receive one PWM signal
  Output one dual-sided PWM signal representing the necessary sine wave
  Have 0 and 100 VDC rails capable of providing 15 A
Three-phase Inverter
  Three single-phase inverters
  Single-phase inputs 120⁰ out of phase from any other input
  Capable of 5 A per phase

## Slide 15: Inverter Updates
IRF520N MOSFETS
  Used for testing of single phase inverter
  Current limiting resistor system protection
  IGBTs will be used when filter, controller, and load are designed and built

## Slide 16: Filter
Used to extract sine wave encoded in PWM signal
Three identical filters used (one for each phase)
LC filter

## Slide 17: Filter

## Slide 18: Filter
LC Filter
Components rated for 400V and 15A
Output sinusoidal waveform extracted from PWM signal

## Slide 19: Load
Overall system output used for testing
Initially resistive-inductive (RL) for both single- and three-phase systems
Final tests will be performed on a three-phase motor
Shall be able to draw the rated power from the system

## Slide 20: Lab Work
Opto-coupler Simulation (6N137)
Gate Driver and Opto-coupler construction
HCPL3120 Gate Driver construction
Single phase, single side inverter test
  With IRF520N MOSFET

## Slide 21: Lab Work
Basic cDAQ Interface
  Analog Input
  Digital Output (TTL)

## Slide 22: Lab Work

## Slide 23: Lab Work
Basic PWM Generation Controller in LabVIEW
Point by Point vs Waveform Signals

## Slide 24: Lab Work

## Slide 25: Equipment & Parts List
LabVIEW Student Edition
NI-cDAQ-9174 Data Acquisition Chassis
NI-9401 Digital I/O
NI-9221 Analog Input Module
NI-9211 Thermal Couple
IR2110/2113
6N137 Opto-coupler
HCPL3120 Gate Driver*
IRF520 MOSFET*
FMG2G75US60 IGBT Pair with anti-parallel diodes
Sources and Scopes available in Power Lab

## Slide 26: Schedule
Schedule |  | 
Week | Date | Task
1 | 1/27/2013 | LabVIEW Tutorials
2 | 2/3/2013 | Build & test single phase optical isolator Build & test single phase gate driver and inverter
3 | 2/10/2013 | 
4 | 2/17/2013 | Interfacing LabVIEW with NI cDAQ
5 | 2/24/2013 | Basic LabVIEW controller design
6 | 3/3/2013 | LC filter design & single phase resistive/inductive load selection
7 | 3/10/2013 | Apply LC filter and load to single phase VFACS
8 | 3/17/2013 | Controller tuning/modification with voltage feedback
9 | 3/24/2013 | Performance testing of single phase VFACS
10 | 3/31/2013 | Re-evaluation of schedule/evaluation of implementing three-phase VFACS
11 | 4/7/2013 | DC to AC source conversion design
12 | 4/14/2013 | DC to AC source conversion building and testing
13 | 4/21/2013 | Final system testing and analysis
14 | 4/28/2013 | Oral Presentation Preparation/ Final Project Report

## Slide 27: Questions?

## Slide 28: Pictures

## Slide 29: Datasheets
http://www.fairchildsemi.com/ds/6N/6N137.pdf
http://www.daedalus.ei.tum.de/attachments/article/257/IR2110_IR2110S_IR2113_IR2113S.pdf
http://pdf.datasheetcatalog.com/datasheet/fairchild/FMG2G75US60.pdf
http://www.datasheetcatalog.com/datasheets_pdf/H/C/P/L/HCPL-3120.shtml
https://www.futurlec.com/Transistors/IRF520.shtml

## Slide 30: Flow Chart

## Slide 31: RLC Filter Design Equations

## Slide 32: RLC Filter Response