## Slide 1: Autonomous Underwater Robots Final Presentation
RYAN LIPSKI, CAMERON PUTZ, AND NICK SIKKEMA
ADVISOR: DR. JOSEPH DRISCOLL
DEPARTMENT OF ELECTRICAL AND COMPUTER ENGINEERING, BRADLEY UNIVERSITY
APRIL 9, 2015

## Slide 2: Outline
Problem statement
Objective and metrics
Functional requirements
Background information
System block diagram
Division of labor
Subsystems
Results
Conclusions

## Slide 3: Problem Statement
Map underwater terrain using multiple autonomous robots
Avoid collisions
Generate a final image of the terrain

## Slide 4: Objectives and Metrics
Objective | Metric
Minimize Cost | Determined by the production cost of one member of the swarm.
Autonomous | The amount of human interaction needed for the swarm to function.
Mobile Underwater | The turn radius of each swarm member and how close the swarm member is to neutrally buoyant.
Durable | The amount of places that fail per swarm member.
Portability | The perceived size and weight of each swarm member.

## Slide 5: Functional Requirements
Functional Requirements
The submarines shall have a battery life of at least 15 minutes.
The swarm shall maneuver through a body of water.
Each submarine shall detect other submarines.
The swarm members shall operate as a swarm when near each other.
The swarm shall take images of underwater terrain.
Each submarine shall surface upon its battery level dropping below 5%.
Software shall create an image that is collected from the individual submarine images.

## Slide 6: Literature Review
AUV history
AUV swarm research
  Cocoro
Swarm of Fish [1]

## Slide 7: Cocoro
Image of Cocoro [3]
Cocoro normal operation [2]

## Slide 8: Blue LEDs - Visibility
Attenuation of ligh in ocean water [4]

## Slide 9: Blue LEDs - Detection
Characteristics of detection methods [4]

## Slide 10: System Block Diagram

## Slide 11: Division of Labor
Cameron – hardware
Camera system
Detection array
Power system
Ryan – hardware and software
Detection array
Motor control
Power system
Nick – software
Camera system
Motor control
Power system

## Slide 12: Detection Array
Block Diagram

## Slide 13: Detection Array
Osram photodiode [5]
Everlight photodiode [6]
Saturation | 36 inches – 4.9 Volts | 4 inches – 4.89 Volts
Max Distance | 180 inches – 0.6 Volts | 132 Inches -- 0.120 Volts
Linearity | Linear | Non-Linear
Ambient Light | 100% Saturation | 29% Saturation
Price | $8.85 | $0.59
Photodiode comparison
Results

## Slide 14: Detection Array
Transimpedance amplifier
Everlight photodiode [6]
Model of photodiode
Design

## Slide 15: Current Source design
Model of 3 W LED
Simulation

## Slide 16: Circuit Layout
Eagle 7.1.0
Boards sent to OSH Park
Photodiode interface board
LED driver board
H-bridge board
Design

## Slide 17: Circuit Layout
Finalized OSH Park boards
Photodiode interface board
LED driver board
H-bridge board
Results

## Slide 18: Camera System
Block Diagram

## Slide 19: Camera System
555 timer [7]
555 timer on perfboard
Results

## Slide 20: Camera System
Camera key fob
Camera interface board
Method

## Slide 21: Camera
With timestamp
Without timestamp
Method

## Slide 22: Camera
Meets spec for 10% gap in final image
Results
Picture of fish tank
Final image

## Slide 23: Power System
Block Diagram

## Slide 24: Power System
Discharge of NiMH batteries [8]
Research

## Slide 25: Power System
Step-up regulator
  Input minimum 2.5 volts
  Output 5 volts
Reference voltage
Noise isolation
Diode
Meets spec for surfacing at 10%
Pololu U3V12F5 [9]
Method

## Slide 26: Motor Control
Block Diagram

## Slide 27: Motor Control
I2C h-bridge (DRV8830)
Single channel, PWM controlled h-bridge
Heatsinking through PowerPADTM
1 A, 2.75 - 6.8 V
Cost: $2.44
DRV8830 [10]
Design

## Slide 28: Motor Control
I2C IMU (LSM303D)
Use the accelerometer
Meets spec for velocity control and using I2C
Design
LSM303D [11]

## Slide 29: Motor Control
Depth tracking
  6 cm dead band
  Testing at 52 cm deep
  PID control
Design
Testing setup in aquarium

## Slide 30: Motor Control
Waterproofing
  Plastic cylinder
  Hot glue
  Epoxy
Waterproofed bottom of sail
Design

## Slide 31: Motor Control
Depth tracking
Results
https://www.youtube.com/watch?v=KP_CVridH08 https://www.youtube.com/watch?v=-tTprnzq--I
https://www.youtube.com/watch?v=9dOgWr1T1QA

## Slide 32: Power System
Block Diagram

## Slide 33: Power System
Battery supply
  4 NIMH AA batteries
    1.34 V per cell
    2500 mAh
  5.36 V: h-bridges, LED drivers and pressure sensor
  4 V: voltage booster → all other hardware
Tenergy AA battery [12]
Design

## Slide 34: Power System
Battery life calculation
  Bench-top test
    Average current draw: 1202 mA
    Estimated run time: 124 minutes
  Battery life spec is 25 minutes
Bench-top current draw
3 batteries
4 batteries
Results

## Slide 35: Power System
Worst case battery life calculation
  All three motors at max duty cycle
    Peak current draw: 1202 + 2550 - 450 = 3302 mA
    Estimated run time: 45 minutes
  Still meets 25 minute spec
Result

## Slide 36: System Test Results
Objective | Metric
Minimize Cost | Determined by the production cost of one member of the swarm.
Autonomous | The amount of human interaction needed for the swarm to function
Mobile Underwater | The turn radius of each swarm member and how close the swarm member is to neutrally buoyant.
Durable | The amount of places that fail per swarm member.
Portability | The perceived size and weight of each swarm member

## Slide 37: System Test Results
Minimize cost

## Slide 38: System Test Results
Autonomous & mobile underwater
https://www.youtube.com/watch?v=wOSrQxpOtXE

## Slide 39: System Test Results
Autonomous & mobile underwater
https://www.youtube.com/watch?v=wOSrQxpOtXE

## Slide 40: System Test Results
Durable

## Slide 41: System Test Results
Portability
  35 cm long
  12.5 cm tall at the sail

## Slide 42: Autonomous Underwater Robots Final Presentation
RYAN LIPSKI, CAMERON PUTZ, AND NICK SIKKEMA
ADVISOR: DR. JOSEPH DRISCOLL
DEPARTMENT OF ELECTRICAL AND COMPUTER ENGINEERING, BRADLEY UNIVERSITY
APRIL 9, 2015

## Slide 43: References
[1] E. Yong, Wired. (2013). How the Science of Swarms Can Help Us Fight Cancer and Predict the Future [Online]. Available: http://www.wired.com/2013/03/powers-of-swarms/all/
[2] CoCoRo Largest AUV swarm 2013 (2013, May 29) [Online]. Available: https://www.youtube.com/watch?v=Hjkmm13Scm4
[3] CoCoRo swarm of underwater Robots (n.d.) [Online]. Available: i.ytimg.com/vi/XUk-qLfiwlc/0.jpg
[4] H. Brundage. “Designing a Wireless Underwater Optical Communication System” unpublished.
[5] Silicon Photodiode for the Visible Spectral Range (2014, Jan 10) [Online]. Available: http://www.osram-os.com/Graphics/XPic3/00101632_0.pdf
[6] RGB Color Light Sensor Surface – Mount (2012) [Online]. Available: http://www.everlight.com/file/ProductFile/201407061648128798.pdf
[7] K. Bigelow (2014). The 555 Timer IC [Online]. Available: http://www.play-hookey.com/digital/555/timer_555.html
[8] LiPo Vs NiMH Batteries, Lipo Manufacturer (2014 Mar.) [Online]. Available: http://lipomanufacturer.blogspot.com/2014/03/lipo-vs-nimh-batteries.html

## Slide 44: References Continued
[9] Pololu 5V Step-Up Voltage Regulator U3V12F5 (n.d.) [Online]. Available: https://www.pololu.com/product/2115
[10] DRV8830 (n.d.) [Online]. Available: http://www.ti.com/product/drv8830
[11] Pololu LSM303D 3D Compass and Accelerometer Carrier with Voltage Regulator (n.d.) [Online]. Available: https://www.pololu.com/product/2127
[12] Tenergy Premium 1.2V 2500mAh Ni-MH AA Rechargeable Battery, (n.d.) [Online]. Available: http://www.tenergy.com/10320
[13] Integrated Silicon Pressure Sensor On-Chip Signal Conditioned, Temperature Compensated and Calibrated (2012, Oct.) [Online]. Available: http://www.freescale.com/files/sensors/doc/data_sheet/MPX5010.pdf
[14] Low-Voltage Motor Driver with Serial Interface, Texas Instruments, [Online]. Available: http://www.ti.com/lit/ds/symlink/drv8830.pdf
[15] S. Sugihara (2014). Three Rules of Swarm Algorithm [Online]. Available: http://igeo.jp/tutorial/43.html
[16] J. YUH (2000). Design and Control of Autonomous Underwater Robots: A Survey [Online]. Available: neuron.tuke.sk/hudecm/PDF_PAPERS/DesignAndControlOfAutonomousUnderwaterrobotsASurvey.pdf

## Slide 45: Research Parts
Pressure sensor
  Package
  Gauge vs absolute
MPAK package [13]
Unibody package [13]
Reasearch

## Slide 46: Collision Detection
Collision detection and tilt compensation

## Slide 47: Software Integration
Combining code for subsystems
  Optimization
  Functional programming style
Doxygen output for the multiplexer
Design

## Slide 48: Regulator Output
Step-up regulator
  Input minimum 2.5 volts
  Output 5 volts
Reference voltage
Noise isolation
Console Output for Regulator and Multiplexer
Result

## Slide 49: Swarming Algorithm
Flowcharts were first design step
Detection zones
Simplified swarming flowchart
Design

## Slide 50: Swarming Algorithm
Multiple iterations before coding
  Zone checking priority
  Integrating with rest of code
Zone checks alter variables that factor into the motor control
  Only applies to X and Y motors
Motors updated after all zones checked
Code runs until low battery voltage is detected
Simplified swarming flowchart
Design

## Slide 51: Circuit and System Layout
Everlight photodiodes
  Planned to solder strands wires to each side
    Difficult to solder without bridging the leads
    2.1 mm between the leads
  Solution: Use small section of straight header pins to extend leads
    Reduces soldering difficulty
    Much more rigid connection
    Plastic section of header pins doubles as a mounting point
Everlight photodiode soldered to section of header pins
Design

## Slide 52: Motor Control and Power
3 DC brushed motors (x, y, z configuration)
  Y motor highest current draw: 860 mA peak draw
    Recorded with only rear propeller submerged
  X and y motor feedback: IMU
  Z motor feedback: pressure sensor

## Slide 53: Detection Array
Bench top detection array
  Baffle configuration testing
    Baffle protrusion distance and LED distance experimented with
    LED swept from 0 to 180° while recording light intensity
Baffle test setup
Baffle
Photodiodes
Experiment

## Slide 54: Detection Array
Left vs right photodiode (5 mm baffle)
Detection zones
Bench top detection array
  Baffle configuration testing
    12cm LED distance
Result

## Slide 55: Compass and Accelerometer
Heading test output
Velocity test output

## Slide 56: Efficiency of Motor [14]

## Slide 57: Step-Up Regulator Efficiency [9]

## Slide 58: Pressure Sensor Output MPX5010 [13]

## Slide 59: Pressure Sensor Circuit Diagram MPX5010 [13]

## Slide 60: Complete Swarming Flowchart

## Slide 61: Circuit and System Layout
Submarine dissection
  Each motor has 2 leads along with a third wire
    Determined to be a ground wire
  Battery compartment has a
  4.8 V, 3.6 V and ground lead
  Switch has 4 leads
    Identified each lead
  First submarine is now prepped for assembly
Complete Swarming Flowchart
Disassembled submarine
Original submarine
Analysis

## Slide 62: Swarming Algorithm
Design of this algorithm is complete
Algorithm can be partially tested on a bench top
Full testing will be possible only when the swarm is constructed
May need to alter weighting of variables or radii of the different zones
Design

## Slide 63: First amplifier design

## Slide 64: Second photodiode design

## Slide 65: 555 Timer Output

## Slide 66: Second design iteration output

## Slide 67: Current Source design

## Slide 68: Circuit Layout
Eagle 7.1.0
First iteration of the detection array surface mount board

## Slide 69: Circuit Layout
Eagle 7.1.0
First library package Everlight photodiode
First library symbol Everlight photodiode

## Slide 70: Circuit Layout
Eagle 7.1.0
  Photodiode board rev. 1

## Slide 71: Circuit Layout
Eagle 7.1.0
  Photodiode board rev. 2

## Slide 72: Circuit Layout
Eagle 7.1.0
  Photodiode board rev.3

## Slide 73: Circuit Layout
Eagle 7.1.0
  Photodiode board rev.4

## Slide 74: Circuit Layout
Eagle 7.1.0
  High current board rev. 1

## Slide 75: Circuit Layout
Eagle 7.1.0
  LED driver board rev. 1

## Slide 76: Circuit Layout
Eagle 7.1.0
  Motor driver board rev. 1

## Slide 77: Eagle Schematic

## Slide 78: Eagle Schematic

## Slide 79: Eagle Schematic

## Slide 80: Constraints
Avoid harming underwater organisms
Battery life
Functional up to two feet of water
Robots must be reasonably sized

## Slide 81: Detection Methods
Acoustic
Electromagnetic
Optical
  Image processing
  LEDs

## Slide 82: Swarming Techniques
Boids
  Simulates the flocking of birds
  Criteria include cohesion, separation and alignment
Principles of swarming [15]
Cohesion
Separation
Alignment

## Slide 83: Swarming Techniques
Minimalistic
  Based upon Boids
  Criteria include cohesion, separation and pseudo-alignment
Principles of swarming [15]
Cohesion
Separation
Alignment

## Slide 84: Assembly/Soldering
Everlight photodiode soldered to section of header pins
LED soldered to section of header pins
Result

## Slide 85: Functional Requirements
Functional Requirement | Specification/Method
Each submarine shall detect other submarines. | 1.22 meters, on PCB's
The swarm shall take images of underwater terrain. | 640x480, compiled image
The swarm shall maneuver through a body of water. | Depth: ± 10 cm, up to 60cm, constant speed ± 5%, I2C controlled
The submarines shall have a battery life of at least 15 minutes. | Battery life: 25 min
The swarm members shall operate as a swarm when near each other. | Passive sensing while close
Software shall create an image that is collected from the individual submarine images. | 10% image gaps or less
Each submarine shall surface upon its battery level dropping below 5%. | Surface at 10% battery life

## Slide 86: Societal Impact
Development is ethical
Aquatic industries/research will be affected
Originally marketed as a toy RC submarine
Submarines will navigate at relatively slow speeds
Boats could collide with the swarm

## Slide 87: Environmental Impact
Low natural resources costs
Lost submarines could pollute the water
Plant life could be disturbed
Large obstacles will be detected and avoided

## Slide 88: Related Patents
CN 102916744 A - Underwater LED visible light communication system
US 20140212142 A1 - Underwater optical communication system
US 20050232638 A1 - Methods and apparatus for underwater wireless optical communication