## Slide 1: SAE Formula Car Data Acquisition & Display System
February 25, 2015
Advisor : Professor Steven Gutschlag
Ahmed Albitar John Gertie
Justin Ibarra Sean Lenz

## Slide 2: Problem Description
Acquire 5 Key data points from SAE Formula Car
  RPM
  Speed
  Oil Pressure
  Water Temperature
  Battery Voltage
Aggressive Notification system to alert driver if data exceeds threshold values
Multi-mode touch screen display
Wireless transmission of data to off-track computer
Data Logger

## Slide 3: Agenda
System block diagram
Division of Labor
Sensor interfacing
Interfacing transceiver with LabVIEW
Interfacing microcontroller with Amulet

## Slide 4: System Block Diagram
Sensors
Microcontroller
(ATmega128)
Amulet LCD
Wireless Transceiver
UART
RS-232
Laptop
(LabVIEW GUI)
UART
5V Power Supply
Notes: Change rs-232 to UART

## Slide 5: Division of Labor
Ahmed
  Sensor selection & interfacing
Justin & John
  Interface microcontroller with HyperTerminal
  Test microcontroller with simulated sensor data
  Interface microcontroller with LabVIEW
Sean
  Prepared LabVIEW to receive wireless data
  Interface microcontroller with Amulet

## Slide 6: System Block Diagram
Sensors
Microcontroller
(ATmega128)
Amulet LCD
Wireless Transceiver
UART
RS-232
Laptop
(LabVIEW GUI)
UART
5V Power Supply
Ahmed
Sean
John & Justin

## Slide 7: Outline for Ahmed
Original Schedule
Subsystem Block Diagram
Updated Schedule
Research
Temperature sensor
Pressure sensor
RPM and velocity sensor
Remaining tasks

## Slide 8: Original Schedule

## Slide 9: Subsystem Block Diagram

## Slide 10: Updated Schedule

## Slide 11: Research
Mechanical Engineering Meetings
  Temperature Sensor
  Dimensions
  Hall-Effect sensor
Cost Analysis

## Slide 12: Current Temperature Sensor
ProSense TTD25N-20-0300F-H
$ 126
Analog output: 4 to 20mA
Operating Voltage: 10 to 30VDC
Temperature range: 0-300 F
¼ NPT
Cable : CD12L-0B-020-A0

## Slide 13: Temperature Sensor Circuitry
Inverting Op-amp

## Slide 14: Temperature Sensor Testing
Within 3 percent accuracy
T = m × Io +k ( Io = V×Rf)
m = 10418.75
k = -59.48
Linear Sensor

## Slide 15: Temperature vs Current graphs

## Slide 16: Current Pressure Sensor
ProSense PTD25-20-0100H
$126
Analog output: 4 to 20mA
Operating Voltage: 9.6 to 32VDC
PSI range: 0 to 100
¼ NPT
Cable : CD12L-0B-020-C0

## Slide 17: Pressure Sensor Circuitry
Inverting Op-amp

## Slide 18: RPM and Velocity Sensor
Mechanical Engineering sensor
Supply voltage: 4.5 - 24 V DC
Supply current: 10 - 20 mA
Output signal type: Pulse 0-50 V
Sensing distance : 0.5 to 2 mm
Operating temperature range: -40 to 150 Celsius

## Slide 19: Remaining Work
Create Sensor’s Circuitry
Test the Sensors
Install the Sensors
Test the System

## Slide 20: Remaining Schedule

## Slide 21: Outline for John & Justin
Subsystem Block Diagram
Schedule/Percentage complete
Hardware & Software Used
Design analysis and approach
ADC Code
Testing with simulated sensor data
Interfacing with LabView
Research conclusion
Results
Remaining Work

## Slide 22: Subsystem Block Diagram

## Slide 23: Schedule
Complete
Incomplete

## Slide 24: Percentage Completed
    100% complete with microcontroller to Aerocomm transceiver communication
    100% complete with Aerocomm transceiver to Aerocomm transceiver wireless communication
    80% complete with wireless transmission to LABview

## Slide 25: Hardware & Software Used
Hardware
Atmega128
Aerocomm AC4790
Laptop
Software
Atmel Studio
HyperTerminal
LabVIEW

## Slide 26: Additional Research Needed
    Familiarize myself with progress John made last semester involving the wireless transmission.
    Look over Aercomm manual to understand how it sends and receives data wirelessly.
    Research how LABview interacts with incoming signals.
    Look over microcontroller datasheet as to understand what each of the pins on it are use for and how they are initialized in code.
    Researching error codes and what most likely cause certain ones we were receiving.

## Slide 27: Design Approach
    Design a system that receives data from incoming signals.
      A to D converter
    Design a system that transmits the data receive wirelessly between two transceivers.
    Design a system that displays the wirelessly sent data values in LABview
      Real time
      Accurate

## Slide 28: Analysis Approach
    First analyze wireless transmission
      Look on hyperterminal to make sure data sent is the correct number of bytes
      Look on hyperterminal to analyze the bytes and make sure the values change as input sensor values change
    Use oscilloscope to view output of pins
      Correct high and low voltage signals.
      Allows us to see the frequency of data being received and sent.
    View data received in LABview to make sure it is same as on hyperterminal.
      Allows us to verify LABview is analyzing incoming signals correctly.

## Slide 29: Cost consderations
    Software
      No new software needed to be purchase
    Microcontroller
      Atmega128 -chip costs about 12$
    Aerocomm AC4790board and transceivers
      Board and transceivers -45$
      Using from previous years projects.

## Slide 30: ADC
Needed to convert sensor data for LabVIEW
ADC code
  Initialization
  Interrupt Service Routine(ISR)
  Ascii function

## Slide 31: Initialization

## Slide 32: ISR

## Slide 33: Testing with Simulated Data
Linear Output
  Oil Pressure, Water Temperature, Battery Voltage
  Simulated with Power Supply
Pulse Output
  Tachometer, Speedometer
  Simulated with the Wave Generator
Notes: include sampling rates

## Slide 34: Interfacing with LabView
Communication Protocol
  Universal Asynchronous Receiver/Transmitter(UART)
Transmission Type
  Ascii
Sent using packets
Notes: more discussion of packets

## Slide 35: LabVIEW Packets
16 byte array
  2 bytes dedicated to water temperature
  2 bytes dedicated to oil pressure
  4 bytes dedicated to MPH
  4 bytes dedicated to RPM
  Other bytes to be used for flags

## Slide 36: Research
Sensor output signal types
Sending packets through Aerocomm
Atmel Studio error codes
Notes: pin signals

## Slide 37: Results
Simulated sensor data displayed in HyperTerminal
LabVIEW interfaced with transceiver

## Slide 38: Remaining Work
Finish interfacing transceiver with LabVIEW display
Finalize microcontroller and interface pc board
Install system on vehicle

## Slide 39: Sean’s Agenda
Schedule
  Gantt Chart
Research
HW/SW Interface
  Serial Communication
    ATmega128 to Amulet LCD
    Aerocomm to LabVIEW
Results
Remaining Work

## Slide 40: Sean’s Schedule
% Completed | Remaining Work
Notes: Add legend

## Slide 41: Research
Amulet serial communication protocol
LabVIEW Instrument I/O Assistant
Troubleshooting errors

## Slide 42: Hardware & Software
Equipment
Amulet LCD
ATmega128 (microcontroller)
Software
GEMstudio Pro (Amulet display software)
Atmel Studio 6.1 (microcontroller software)
LabVIEW 2014

## Slide 43: Amulet LCD
Serial Protocol
  UART
  Ascii
  9600 bps baud rate
  Transmit specific protocol to access variables
Microcontroller is master
  Initializes communication
Amulet is slave
  Full Protocol- Responds only if Amulet receives valid message

## Slide 44: Amulet LCD
Internal RAM (IR) is memory on the Amulet.
  256 byte variables
  256 word variables (word = 2 bytes)
  199 string variables
Can receive 14 different command messages from microcontroller
  Can access internal RAM on Amulet
  Changing and copying variables
  Jump to different pages on display
  Draw pixel, line, or box

## Slide 45: Amulet Serial Communication Flow Chart
Op-code
Variable Address
(High nibble)
Variable Address
(Low nibble)
Variable Value
(High nibble)
Variable Value
(Low nibble)
Op-code = Tells Amulet what type of variable is being accessed (byte or word)
Address = The variables location on the RAM of the Amulet LCD
Value = The data to be displayed on the Amulet LCD
Figure 1 – Transmit protocol for a byte variable.

## Slide 46: Amulet Protocol Ascii
Example: microcontroller sets internal RAM (IR) word variable to specific value (0x02C9)
Figure 3 – Serial communication flow chart

## Slide 47: UART Transmit
1V per division
0.5ms per division
Transmission contains:
{0x00, 0xD6, 0x31}

## Slide 48: LabVIEW GUI
Serial Protocol
  RS-232
  Ascii
  9600 baud rate
  Transmit packages of data
Instrument I/O Assistant
Front Panel vs. Block Diagram
Connect blocks to data type and viewing method
Aerocomm
Transceiver
Laptop
(LabVIEW GUI)
Instrument I/O Assistant
Display Data
Save Data

## Slide 49: Front Panel

## Slide 50: Serial Communication Setup

## Slide 51: Block Diagram

## Slide 54: Results
Successful interface between ATmega128 and Amulet LCD
  Data sent and displayed on the Amulet LCD
Successful interface between Aerocomm Transceiver and LabVIEW GUI
  Data sent and displayed on the LabVIEW GUI

## Slide 55: Remaining Work
LabVIEW
  Set up data log feature
  Connect data to graph results over time
Simulations to test system (on LabVIEW and Amulet LCD)
  From function generator
  From sensors
Hardware/Software Interface
  Power supply circuitry for Amulet

## Slide 56: Questions?

## Slide 57: Appendix

## Slide 58: Initialization

## Slide 59: ISR

## Slide 60: .C/.h files

## Slide 61: to_ascii

## Slide 63: Atmega128 Electrical Characteristics
Vcc = 3.3V

## Slide 64: 3.3V Logic Levels (TTL)
Voh – output high
Vih – input high
Vol – output low
Vil – input low
Vcc – power supply
Gnd - Ground

## Slide 65: Amulet Ascii Transmit Protocol Example
Microcontroller Set Byte Variable
Amulet Response
Microcontroller Set Word Variable
Amulet Response
Figure 2 – Serial communication flow chart

## Slide 67: UART Receive (Echo)
1V per division
1ms per division

## Slide 68: UART Transmit/ECHO
Blue: Transmit
Purple: Receive
1V per division
2.5ms per division