## Slide 1: 3D Environmental Mapping and Imaging for AUVSI RoboBoat
David Bumpus, Dan Kubik, & Juan Vazquez
Advisor: Dr. José Sánchez
Customer: Mr. Nick Schmidt
Department of Electrical & Computer Engineering
April 26, 2016

## Slide 2: Presentation Outline
Problem Background
Functional Requirements
Project Overview
Division of Labor
  Juan Vazquez
  Dan Kubik
  David Bumpus
Conclusion

## Slide 3: Presentation Outline
Problem Background
Functional Requirements
Project Overview
Division of Labor
  Juan Vazquez
  Dan Kubik
  David Bumpus
Conclusion

## Slide 4: Problem Background: Motivation
Since 2013, Bradley has twice sent teams to the AUVSI RoboBoat competition
Teams have difficulty determining distances to objects from boat
Fig. 1. Potential RoboBoat paths
Fig. 2. Navigating through buoys

## Slide 5: Problem Background: Motivation
Fig. 3. Boat identifying area of interest [1]

## Slide 6: Problem Background: Objective
Create an accurate measurement system that:
  Measures distance to objects in the boat’s surroundings
  Uses lidar
  Operates in real-time
  Is easy to use for future boat teams

## Slide 7: Problem Background: Significance
Lidar
  “light” + “radar”
  Distance and amount of light (reflectivity)
  Reduces human error
Fig. 4. Application of lidar for automobile navigation [2]

## Slide 8: Presentation Outline
Problem Background
Functional Requirements
Project Overview
Division of Labor
  Juan Vazquez
  Dan Kubik
  David Bumpus
Conclusion

## Slide 9: Functional Requirements
System must:
  Obtain and store lidar data
  Obtain camera images
  Reduce lidar dataset as instructed
  Register lidar data with image data
  Create color overlay image representing distance
  Determine nearest object location and distance
Fig. 5. A color overlay image representing registered distance information [3]

## Slide 10: Presentation Outline
Problem Background
Functional Requirements
Project Overview
Division of Labor
  Juan Vazquez
  Dan Kubik
  David Bumpus
Conclusion

## Slide 11: Project Overview
Fig. 6. System block diagram

## Slide 12: Presentation Outline
Problem Background
Functional Requirements
Project Overview
Division of Labor
  Juan Vazquez
  Dan Kubik
  David Bumpus
Conclusion

## Slide 13: Division of Labor
Data Acquisition
  Juan
Data Organization
  Dan
Data Processing
  David
Fig. 7. Captain [4]

## Slide 14: Presentation Outline
Problem Background
Functional Requirements
Project Overview
Division of Labor
  Juan Vazquez
  Dan Kubik
  David Bumpus
Conclusion

## Slide 15: Juan Vazquez: Overview
Fig. 8. Subsystems covered in purple

## Slide 16: Juan Vazquez: OS Installation
Ubuntu Server
  Size
  Software availability
  Configurability
Fig. 9. Ubuntu Server [5]

## Slide 17: Juan Vazquez: OS Installation
Operating system booting
  MicroSD
  EMMC (Embedded MultiMediaCard)
Establishing network connection
  Ethernet connection bridge
Fig. 10. MicroSD [6]
Fig. 11. EMMC [7]

## Slide 18: Juan Vazquez: Camera Interface
Logitech C500 Linux driver
Open Source Computer Vision
  Supports Linux
  C++ Interface
  Video capture
  Image registration
Fig. 12. OpenCV [8]

## Slide 19: Juan Vazquez: Camera Interface
Image capture program
  Live video read
  Continuously capturing/overwriting
  Stores in PPM (Portable Pixmap Format)
Fig. 13. Logitech C500 [9]

## Slide 20: Juan Vazquez: VLP-16 Interface
Libpcap
  Library for packet capture
Packet Detection
  UDP (User Datagram Protocol)
Packet Storage
  Text file
Fig. 14. VLP-16 [10]

## Slide 21: Juan Vazquez: Detection & Read Interface
Fig. 15. Removing Unwanted Data

## Slide 22: Presentation Outline
Problem Background
Functional Requirements
Project Overview
Division of Labor
  Juan Vazquez
  Dan Kubik
  David Bumpus
Conclusion

## Slide 23: Dan Kubik: Overview
Fig. 16. Subsystems covered in purple

## Slide 24: Dan Kubik: Reading lidar data
Data point
Each text file contains an encoded packet of lidar data
“ FF | EE | 7D | 70 | 6F | 06 | 02 | F3 | 06 …”
Initial flag
Azimuth
Distance
Reflectivity
Fig. 17. Azimuth and altitude explained [11]

## Slide 25: Dan Kubik: Reading lidar data
Data packet:
Fig. 18. Information in a data packet
Initial Flag
FFEE
Data point:
Distance
Reflectivity
Altitude
x 16
Azimuth
x 24
Time stamp
Scanner Information

## Slide 26: Dan Kubik: Organizing lidar data
Hierarchy of C++ classes:
MasterBlock
Data block
Half data block
Data packet
Data point
Highest level
Lowest level

## Slide 27: Dan Kubik: Organizing lidar data
MasterBlock – internal “interface”
  Considers incoming data
  Stores if data falls within “frontal” or “selection” ranges
  Fills up to one 360° sweep of data
Fig. 19. Top down view: example of a selection range
0°
225°
315°

## Slide 28: Dan Kubik: Data flow
Fig. 20. Subsystem Flowchart

## Slide 29: Dan Kubik: Data flow
Fig. 20. Subsystem Flowchart

## Slide 30: Dan Kubik: Data flow
Fig. 20. Subsystem Flowchart

## Slide 31: Dan Kubik: Data flow
Fig. 20. Subsystem Flowchart

## Slide 32: Dan Kubik: Data flow
Fig. 20. Subsystem Flowchart

## Slide 33: Dan Kubik: Data flow
Fig. 20. Subsystem Flowchart

## Slide 34: Dan Kubik: Data flow
Fig. 20. Subsystem Flowchart

## Slide 35: Dan Kubik: Organizing lidar results
Fig. 23. 3D-Viewer view of box, created from MasterBlock object
Fig. 22. VeloView view of box
Fig. 21. Scanned cardboard box [12]

## Slide 36: Dan Kubik: Organizing lidar results
Fig. 24. Full 360° view, input: (0, 359)
Fig. 25. Frontal 180° view, input: (270, 90)
Fig. 26. Frontal 90° view, input: (315, 45)

## Slide 37: Dan Kubik: Creating color overlay
?
Fig. 27. Creating 2D color range image from 3D lidar data

## Slide 38: Dan Kubik: Barnes Interpolation
30s
40s
50s
60s
70s
80s
Fig. 28. Interpolating unevenly distributed data to a complete grid [13]

## Slide 39: Dan Kubik: Creating color overlay
How to get to two dimensions?
  Convert spherical to rectangular coordinates (X, Y, Z)
  Keep X (horizontal) and Z (vertical) dimension
  Use distances as interpolation values
Fig. 29. Spherical to rectangular coordinates, remove y dimension [14]

## Slide 40: Dan Kubik: Overlay creation results
Fig. 30. Renaissance Coliseum setup
Fig. 31. Renaissance Coliseum lidar data (frontal 90°)

## Slide 41: Dan Kubik: Overlay creation results
Fig. 32. Renaissance Coliseum lidar data (frontal 90°)
Near
Far
Fig. 33. Barnes Interpolation with color thresholding

## Slide 42: Dan Kubik: Overlay creation results
0 m
1.8 m
3.5 m
5.3 m
7.0 m
8.8 m
10.5 m
12.2 m
14.0 m
First column: 11.2m
Third column: 11.8m
Right buoy: 8.26m
Back wall: 15.1m
X Center column: 10.2m (off by 0.3m)
X Left buoy: 7.87m (off by a significant margin)
Fig. 34. Barnes Interpolation of Renaissance Coliseum

## Slide 43: Presentation Outline
Problem Background
Functional Requirements
Project Overview
Division of Labor
  Juan Vazquez
  Dan Kubik
  David Bumpus
Conclusion

## Slide 44: David Bumpus: Overview
Fig. 35. Subsystems covered in purple

## Slide 45: Work Accomplished: Object Detection
Scale Invariant Feature Transform (SIFT)
  Keypoint detection for object detection
  Registration of Barnes interpolation with webcam image
Fig. 36. OpenCV Logo [8]
Fig. 37. A color overlay image representing registered distance information [3]

## Slide 46: SIFT Keypoint Explanation [7]:
Robust against changes in scale or rotation of an image
Fig. 38. Robust SIFT matching [15]

## Slide 47: SIFT Keypoint Explanation [7]:
Step 1: Scale Space Extrema Detection
Difference of Gaussian
Subtract
Result =
Fig. 39. Difference of Gaussian for different octaves in Gaussian pyramid [16]

## Slide 48: SIFT Keypoint Explanation [7]:
Step 1: Scale space extrema detection
Fig. 40. Difference of Gaussian explanation [17]
Subtract

## Slide 49: SIFT Keypoint Explanation [7]:
Step 2: Keypoint localization
Eliminate low contrast keypoints
Eliminate keypoints on edge of image
What remains are strong keypoints
Fig. 41. Eliminate weak keypoints [15]

## Slide 50: SIFT Keypoint Explanation [7]:
Step 3: Orientation assignment
Gradient magnitude and direction is calculated
Create keypoint with same location and scale, but different direction
Fig. 42. Rotation invariant keypoint orientation assignment [15]

## Slide 51: SIFT Keypoint Explanation [7]:
Step 4: Keypoint descriptor
Generate unique histogram with 128 bins for each keypoint
Step 5: Keypoint matching
Search target image keypoints for similar descriptors
Fig. 43. Keypoint descriptor matching

## Slide 52: Work Accomplished: Image Keypoints
Fig. 44. SIFT keypoint detection C++ implementation

## Slide 53: Work Accomplished: Point Cloud Keypoints
Point Cloud Library (PCL)
Open source point cloud processing
Linux compatible
SIFT algorithm
Fig. 45. Point Cloud Library (PCL) logo [18]

## Slide 54: Work Accomplished: Point Cloud Keypoints
Fig. 46. SIFT keypoint detection in point clouds for object detection
Ball
Shadow
Backpack
Closet
Chair
Chalkboard

## Slide 55: Presentation Outline
Problem Background
Functional Requirements
Project Overview
Division of Labor
  Juan Vazquez
  Dan Kubik
  David Bumpus
Conclusion

## Slide 56: Conclusion
Juan
  Lidar Ethernet detection, image capture
Dan
  Data storage and organization, depth overlay for image
David
  Nearest object algorithm development

## Slide 57: Conclusion
  Difficulty acquiring data packets
    Incoming data: speed of incoming data vs. read time
  Lack of precision in Barnes interpolation

## Slide 58: Conclusion
Fig. 47. Registration concept to improve precision of Barnes interpolation

## Slide 59: Conclusion
  Achievements:
    Interfaced camera and laser scanner with Odroid XU4
    Detected nearest objects with 95% accuracy
    Generated depth overlay
Fig. 48. Object detection
Fig. 49. Depth overlay

## Slide 60: 3D Environmental Mapping and Imaging for AUVSI RoboBoat
David Bumpus, Dan Kubik, & Juan Vazquez
Advisor: Dr. José Sánchez
Customer: Mr. Nick Schmidt
Department of Electrical & Computer Engineering
April 26, 2016

## Slide 61: Additional Slides

## Slide 62: Testing of VLP-16 Puck™
Install Veloview Software
Test acquisition of data to Veloview and verify distances
Familiarize self with Veloview data manipulation
Fig. 50. Data acquisition to Veloview using VLP-16 Puck

## Slide 63: Testing of Logitech C500 Webcam
Install Logitech software
Capture images and Video
Fig. 51. Color image from Logitech C500

## Slide 64: Registration Flowchart
Fig. 52. Registration method flowchart [19]
Filter point cloud
Interpolate point cloud
Create depth maps
Feature detection
Outlier elimination
Feature matching

## Slide 65: EMMC vs. microSD Card
Fig. 53. Write/Read Speed Comparison [20]

## Slide 66: UDP Detection
Fig. 54. VLP-16 UDP Detection [21]
Current Packet Sniffer Detection
  TCP (Transmission Control Protocol)
  UDP (User Datagram Protocol)
  ICMP (Internet Control Message Protocol)
  IGMP (Internet Group Management Protocol)
  Others (Detects all Ethernet Frames)

## Slide 67: Ubuntu Desktop vs. Server
Fig. 55. Ubuntu Desktop Requirements [22]
Fig. 56. Ubuntu Server Requirements [23]

## Slide 68: Creating a Bootable MicroSD Card
MiniTool Partition Wizard
  Partition creation and wiping
7zip
  Extraction of IMG.XZ file
Win32 Disk Imager
  Writing the unpacked IMG file to Micro SD card
Process can also used for flashing eMMC

## Slide 69: OpenCV System Requirements [24]
Operating System: Windows, Linux or Mac
Memory (RAM): 256 MB
Hard Disk Space: 50 MB
Processor: 900 MHz

## Slide 70: JPG, PNG, & PPM Comparisons [25] [26]
JPG (Joint Photographic Experts Group)
  Supports 24-bit color RGB
  Compress image data by reducing sections of images to blocks or pixels
  Compression is permanent
PNG (Portable Network Graphics)
  Supports transparency, 8-bit color, and 24-bit color RGB
  Largest of three compared formats
PPM (Portable Pixmap Utilities)
  Lowest common denominator color image file format
  Includes basic color
  Easy to format to process

## Slide 71: Webcam Image Properties

## Slide 72: Read/Write Future Development
Data acquisition currently executing from EMMC
  Directly affects read/write cycles
  Performance will gradually deteriorate
Possible Solution
  Utilize embedded device (Odroid-XU4) RAM
  Shared memory
  Use pipelines or signals to perform writing and storage

## Slide 73: Data Diagram: Velodyne User’s Manual

## Slide 74: Storage Classes
MasterBlock (“Interface”) – Flexible size
  Ensures full 180° view and selected range are received
  Keeps track if 360° worth of data has been checked yet
  Contains multiple HalfDataPackets (as many as needed from one 360° sweep) taken from DataPackets
DataPacket: contains 12 DataBlocks and a time stamp
DataBlock: contains 2 HalfDataBlocks
HalfDataBlock: contains 16 DataPoints and an azimuth
DataPoint: contains one distance, reflectivity, and alt. ang.

## Slide 75: Decoding lidar data
“ FF | EE | 7D | 70 | 6F | 06 | 02 | F3 | 06 …”
Calculating azimuth or distance:
        Flip and combine bytes: 0x707D
        Convert to decimal: 28797
        Divide by 100: 287.97°
Reflectivity is a direct hexadecimal to decimal conversion
Initial flag
Azimuth
Distance
Reflectivity

## Slide 76: Reflectivity
Fig. 57. Reflectivity value meanings [21]

## Slide 77: Visually comparing picture to interpolation

## Slide 78: Barnes Interpolation
30s
40s
50s
60s
70s
80s
Distance value in grid: g(x,y) = , [13]
where:
,
M is the number of known values,
r is the radius to known value from grid point,
k is the “weight factor”,
(x,y) are the coordinates of griddled data,
f is the value of the known datum.

## Slide 79: SIFT Keypoint Explanation:
Fig. 58. Computation of SIFT Keypoints [27]
First, compute gradient magnitude and orientation at each sample point around a keypoint
Use Gaussian window to provide weight to gradients
SIFT keypoint descriptors are basically a histogram of gradient orientations

## Slide 80: SIFT Keypoint Explanation
Fig. 59. Computation of SIFT Keypoints [27]
SIFT descriptors have 128 dimensions at each keypoint resulting in a 128 element vector
Each keypoint descriptor is unique and can be matched to similar descriptors collected from the target image for registration

## Slide 81: Constraints (1 of 2)
Operating voltage less than 12 V
Weight less than 3.6 kg
Current draw less than 4 A
Power consumption less than 50 W

## Slide 82: Constraints (2 of 2)
Must fit within a 10 inch cube
Scanning time of less than 5 sec
Measures a horizontal distance of 9.1 m or greater
Measures a vertical distance of 3 m or greater
Operates for at least 40 minutes

## Slide 83: Non-functional Requirements
System should be:
Weatherproof
Easy to configure
Mechanically stable
Lightweight
Quick, both computationally and in terms of acquisition

## Slide 84: Metrics

## Slide 85: Resources
[1] https://cdn-business.discourse.org/uploads/openrov/original/2X/3/33461a8e6b312ad84c17f7d0050241c34ef0cd70.jpg
[2]http://delphi.com/images/default-source/feature-stories/delphi-lidar-how-it-works.jpg?sfvrsn=2
[3] http://pointclouds.org/documentation/tutorials/_images/range_image1.jpg
[4] http://images.maskworld.com/is/image/maskworld/bigview/captain-professional-beards-made-of-real-hair--103724-kapitaen-captain-beard-bart.jpg
[5] http://www.laybourn.org/index.php/sample-page/
[6] http://www.techwaredist.com/wordpress/index.php/740/
[7] http://www.hardkernel.com/main/products/prdt_info.php
[8] https://upload.wikimedia.org/wikipedia/commons/thumb/3/32/OpenCV_Logo_with_text_svg_version.svg/390px-OpenCV_Logo_with_text_svg_version.svg.png
[9] http://www.engadget.com/products/logitech/webcam/c500/
[10] http://velodynelidar.com/vlp-16.html
[11] https://upload.wikimedia.org/wikipedia/commons/f/f7/Azimuth-Altitude_schematic.svg
[12] http://kidfun.com.au/images/8671140212.JPG
[13] Stanley L. Barnes, “A Technique for Maximizing Details in Numerical Weather Map Analysis,” Journal of Applied Meteorology, vol. 3, pp. 396–409, 1964.

## Slide 86: Resources
[14]https://www.google.com/url?sa=i&rct=j&q=&esrc=s&source=images&cd=&ved=0ahUKEwjOpPiYjavMAhVDVj4KHZroAcwQjBwIBA&url=http%3A%2F%2Fwww.learningaboutelectronics.com%2Fimages%2FSpherical-to-cartesian-rectangular-coordinate-system.png&bvm=bv.120551593,d.d2s&psig=AFQjCNGsMBHcwGyMXJ8RNEeLFh0ZBIztLw&ust=1461718847423110
[15] http://www.mathworks.com/matlabcentral/answers/uploaded_files/16605/lena.jpg
[16] http://eric-yuan.me/wp-content/uploads/2013/10/sift1.jpg
[17] http://www.cs.princeton.edu/~andyz/ip/proj3/img/stack5.jpg
[18] http://pointclouds.org/assets/images/contents/logos/pcl/pointcloudlibrary_vert_large_pos.png
[19] Lv, Fang, and Kan Ren. "Automatic Registration of Airborne LiDAR Point Cloud Data and Optical Imagery Depth Map Based on Line and Points Features." Infrared Physics & Technology 71 (2015): 457-63. Web.
[20] http://www.hardkernel.com/main/products/prdt_info.php
[21] http://velodynelidar.com/docs/manuals/VLP-16%20User%20Manual%20and%20Programming%20Guide%2063-9243%20Rev%20A.pdf
[22] https://help.ubuntu.com/community/Installation/SystemRequirements
[23] http://getintopc.com/softwares/development/opencv-free-download/
[24] http://getintopc.com/softwares/development/opencv-free-download/
[25] http://netpbm.sourceforge.net/doc/ppm.html
[26] http://www.howtogeek.com/howto/30941/whats-the-difference-between-jpg-png-and-gif/

## Slide 87: Resources
[27] https://littlecheesecake.files.wordpress.com/2013/05/sift2.png